## Slide 1
Flexible Manufacturing
  Common Sheet Metal Seams

## Slide 3: Seam
A joint formed by two pieces of metal, overlapped and held in place by spot welds, rivets, or bends.

## Slide 4: Helm
This is the edge of a piece of metal that is folded over on itself for strength and smoothness.

## Slide 5: Flange
This is an edge folded to a 90° angle to make a corner or part of a seam.

## Slide 6: Wire Rolled Edge
This is the edge of a piece of metal that is wrapped around a piece of wire. It makes a stronger, smoother, reinforced edge.

## Slide 7: Simple Seams
These seams will be welded, riveted, or glued to hold them together.
Flat Lapped Seam
Corner Lapped Seam

## Slide 8: Flat Locked Seam
The edges are folded over and slid together to lock the seam.

## Slide 9: Grooved Locked Seam
The edges are folded over and slid together. A hand groover is used to flatten the seam to lock it together.

## Slide 10: Standing Edge Seam
A seam used in roofing to seal the edges of the metal panels.

## Slide 11: Single Bottom Seam
This is a seam used to seal a bottom into a part.

## Slide 12: Examples of Items Made Using Seams

## Slide 13: Tools and Equipment

## Slide 14: Tin Snips
A hand tool to shear sheet metal. They have long handles and short sturdy cutting jaws.

## Slide 15: Aviation Snips
Aviation snips have compound handles, and are made to cut sheet metal easier than regular snips.
Color-coded handles identify the way they cut circles and curves.
Green Right
Red Left
Yellow Straight

## Slide 16: Hand Seamer
This is a plier-style tool with wide jaws, used to bend seams on sheet metal. Some hand seamers have adjustments for depth of a bend.

## Slide 17: Hand Groover
This is a tool used to flatten a seam. The hand groover fits the seam and forces the seam flat, locking it together.

## Slide 18: Sheet Metal Shear
A foot operated shear is used to cut larger sheets of metal.

## Slide 19: Sheet Metal Shear Safety
Keep fingers away from hold down and cutting edge.
Keep your foot away from the treadle of the shear.

## Slide 20: Spot Welder
A resistance spot welder heats a spot, melting the area together, which welds the two pieces of metal together.

## Slide 21: Box and Pan Brake
This is a machine used to bend folds of sheet metal to form seams and sides of projects.

## Slide 22: Safety First
  Always wear personal protective equipment (PPE).
  Always use the tools and equipment safely.

## Slide 23: Assignment #1
Using eight pieces of 3” X 5” sheet metal form the following:
  ¼” Helm
  corner lapped seam
  flat locked seam
  grooved locked seam
  standing seam

## Slide 24: Assignment #2
Construct a Small Sheet Metal Box.

## Slide 26: Layout
Use the Small Sheet Metal Box Plan and draw the layout on the sheet metal.

## Slide 27: Cut Out Box
Using snips, cut the box out. Do Not Cut the seams and helms off.

## Slide 28: Fold Side and Seams
Fold the first side with seams, using a box and pan brake.

## Slide 29: Fold Second Side
Fold the second side.

## Slide 30: Fold First End
Fold the helms of both ends down, then fold the ends up into place.
The seam flanges should fold into the inside of the box.

## Slide 31: Fold Second End
Fold the second end up in place, make sure that the seam flanges fold inside the box.

## Slide 32: Fold the Last Two Helms
Fold the last two helms into the box, locking the side seams in place.

## Slide 33: Finished Box
The box is completed. The top edges should be smooth because of the helms.
Turn in the box and worksheets for a grade.

## Slide 34: Rubrics for Assignment #I
Example # | Name of Seam | Smooth bend (3 pts) | Correct development (8 pts) | Label (4 pts) | Total
1 | ¼” helm |  |  |  | 
2 | Corner lapped seam |  |  |  | 
3 | Flat locked seam |  |  |  | 
4 | Grooved locked seam |  |  |  | 
5 | Standing seam |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
 |  |  |  | Total | 

## Slide 35: Rubrics for Assignment #2
Small Sheet Metal Box Points
1. The box is the size specified in the plans. ___ Yes (12 points) ____ No (0 points) ___________
2. The seams are the correct size. (4 seams; 4 points for each smooth bend) ___________
3. The helms are the correct size. (4 helms; 4 points for each smooth bend) ___________
4. The seams are correctly bent. (4 seams; 2 points for each smooth bend) ___________
4. The helms are correctly bent. (4 helms; 2 points for each smooth bend) ___________
5. The bends are smooth. (8 bends; 5 points for each smooth bend) ___________
Total ___________
Comments______________________________________________________________________
_______________________________________________________________________________
_______________________________________________________________________________
_______________________________________________________________________________
_______________________________________________________________________________